## Slide 1
AareML
Predicting River Water Quality in Swiss Catchments
CAS Advanced Machine Learning — Final Project
June 2026 · University of Bern

## Slide 2
The Problem
Dissolved oxygen (DO) is the primary stress indicator for river ecosystems — drops below 6 mg/L cause fish stress
Swiss rivers face increasing thermal stress from climate change
Current monitoring is reactive — no multi-day predictive capability
14-day
forecast horizon
early warning window

## Slide 3
Data & Experimental Setup
Dataset
CAMELS-CH-Chem
(Nascimento et al. 2025)
17 Swiss gauges
Daily records: 1981–2020
4 features: temp, pH, EC, DO
Experimental Setup
Split:
Train 1981–2014
Val 2015–2016
Test 2017–2020
Model:
Seq2Seq LSTM
LOOKBACK = 21 days
HORIZON = 14 days

## Slide 4
Seq2Seq LSTM Architecture
Encoder
21-day lookback
→
hidden state
Decoder
14-day forecast
→
DO predictions
Key Design Choices
Teacher forcing with linear decay schedule
Optuna hyperparameter search — 75 trials
3-seed ensemble for variance estimation
Optuna Search Space
hidden_size: 64–256
num_layers: 1–3
dropout: 0.1–0.4
lr: 1e-4 – 1e-2

## Slide 5
Single-Site Results — Gauge 2473
Model | RMSE (mg/L) | KGE
Persistence | 0.339 | 0.930
Climatology | 0.332 | 0.853
Ridge Regression | 0.303 | 0.908
VAR(7) | 0.299 | 0.911
LSTM (Optuna) ★ | 0.303 | 0.945
Key Insight
LSTM matches VAR(7) on RMSE but leads on KGE
0.945 vs 0.911
Superior distributional fidelity

## Slide 6
Zero-Shot Transfer to 11 Swiss Gauges
0.451 mg/L
mean zero-shot RMSE
0.568 mg/L
Ridge zero-shot
baseline comparison
0.390 mg/L
Per-gauge retrain
with fine-tuning
0.435 mg/L
EA-LSTM
with static attributes
Wilcoxon: p = 0.037, n = 10 (uncorrected)

## Slide 7
Temperature Prediction
DO Temperature Forecast
Zero-shot
2.598°C
→
EA-LSTM
1.360°C
47% improvement
EC Proxy Analysis
Temp + EC features
1.414°C RMSE
Temperature-only
1.451°C RMSE
2.6% gain from adding EC as proxy feature

## Slide 8
Cross-Ecosystem & Cross-Continental Transfer
Lake Mendota (nb06)
2.962 mg/L
Zero-shot RMSE
NSE = −2.145 — FAILED
Swiss Lakes (nb10)
0.768 mg/L
Retrained RMSE
Zero-shot: 3.980 mg/L → retrained ✓
USGS US Rivers (nb08)
1.368 mg/L
Mean zero-shot RMSE
4.5× harder than Swiss rivers
Key Finding: Domain-specific retraining essential for lake transfer

## Slide 9
Independent Benchmarks
NeuralHydrology EA-LSTM
Multi-gauge (11 sites):
Mean RMSE: 0.512 mg/L
NSE: 0.756
Gauge 2473:
RMSE: 0.407 mg/L, NSE: 0.816
Supports feasibility of seq2seq approach
Cascaded Model (DO = linear(T) + residual)
Gauge 2473 comparison:
Setup A: 0.872 mg/L
Setup B: 0.893 mg/L
LSTM: 0.303 mg/L
LSTM already captures Henry's Law implicitly — no cascading needed

## Slide 10
Conclusions & Next Steps
Key Findings
Seq2Seq LSTM: RMSE = 0.303 mg/L, KGE = 0.945 at gauge 2473 — comparable to VAR(7) on RMSE, superior on dynamics
Zero-shot transfer to 11 gauges: 0.451 mg/L (p = 0.037 vs Ridge, uncorrected)
EA-LSTM temperature: 47% improvement over zero-shot (1.360°C)
Lake transfer fails without retraining — ecosystem boundaries matter
Next Steps
Real-time AWEL data integration
PFAS monitoring pipeline
7-day operational system (AquaSentinel AI)
github.com/polar-bear-after-lunch/AareML · v1.34 · June 2026